## Slide 1: Managing oak adjunct
A practical approach

## Slide 2: WHY, WHEN & HOW CAN WE USE OAK ADJUNCTS
WHY  economic, logistic, practicality
WHEN  is there really a good time to start?
HOW  where do you start? With what?

## Slide 3: THE REASONS
SPACE :
  Stacked 5 high the need is 3.4 sq ft/bbl or for every 110T – additional 1,000 sq ft)
  You want to scale up without increasing your footprint
PRACTICALITY
  Barrels are “high-touch” – frequent topping, washing, steaming, etc…
  Control the level of integration – use staves, blocks or chips (if you don’t have time for long aging, there is something for what you need)
  ECONOMICS
  Reduced labor cost (even for moderately sized wineries) : ex: steaming 3,000 barrels for 4 min each = 200 hours (5 weeks)
  Price of the oak

## Slide 4: QUICK PRICE ANALYSIS (15% new oak equivalent)
CHIPS |  | $/kg |  | g/L | $/Kgal
 |  | $ 14.52 |  | 1 | $ 54.96
 |  |  |  | 1.25 | $ 68.70
 |  |  |  | 1.5 | $ 82.44
STAVES |  | $/unit |  | staves/Kgal | $/Kgal
 |  | $ 7.30 |  | 52 | $ 379.60
BARREL |  | $/unit |  | bbl/Kgal | $/Kgal
 |  | $ 1,100.00 |  | 2.5 | $ 2,750.00

## Slide 5: HOW TO IMPLEMENT A STAVE/BLOCKS/CHIPS PROGRAM
Don’t be afraid to do trials at scale.
Do trials now, for potential implementation in 2 years from now (ie Try even if you don’t think you need it).
Try chips first, tune in to each supplier flavor profile.
Have a good understanding of what your needs are:
Is that wine going to be blended with barrels aged wine?
Is it part of a blend? Is I a stan-alone wine?
Are you looking for aromatics or structure?

## Slide 6: ADDED BENEFITS
More sustainable (many blocks and chips are made from wood that didn’t meet the specs for barrel staves)
Better control of your end-product (it is more manageable to track a 2,000 gallons tank than a 33 barrels lot)
Barrel maintenance is demanding, risk of spoilage often comes from barrels.

## Slide 7: CONCLUSION
If you’re planning to grow, consider adding some oak adjunct to your program.
Or if for nothing else, be curious
Next in your exploration journey: micro-ox