## Slide 1
Sustainability & Efficient Winery Practices – Do More With Less
Stephan Sommer

## Slide 2
Chart Title
Tartrate stability
Protein removal strategies

## Slide 3
Chart Title
Precipitation of crystals (especially tartrate) at different stages during winemaking
Stability influenced by different factors (pH, alcohol, temperature, other macromolecules)
Crystal stability influences other macromolecules as well (proteins for example)
In most cases stabilization possible (cold stabilization, fining or stabilizing agents)

## Slide 4
Available methods for tartrate stabilization
Cold stabilization (with or without seed crystals)
Gum Arabica
Ion exchange
Electrodialysis
Mannoproteins
Carboxymethyl cellulose
Potassium Polyaspartate (KPA)
Metatartaric acid
(max. 1.9 g/L)
(multiple restrictions)
(must not alter character)
(max 100 mg/L)
(max. 100 mg/L)

## Slide 5
Cold stabilization
Source: Neradt (1980)
https://www.ariduswineco.com/
Cool close to freezing point for 3 days up to 3 weeks
minimizes solubility of KHT (limited effect on CaT)
Time and energy consuming
Contact crystals increase efficiency (4 g/L, stir for 5h), can be reused but reduced effectiveness
Stirring and clarification present risk of oxidation and aroma loss

## Slide 6
Gum Arabica
Highly branched polysaccharide from tree sap
Protective colloid  prevents agglomeration of wine components
Non-specific additive  tartrate stability only side effect
Based on observation that crystals mostly precipitate first, followed by proteins and other compounds
Limited relevance as more specific additives become available

## Slide 7
Ion exchange
Source: Rhein and Neradt (1979)
Resin polymer loaded with ions to replace either K+, tartrate, or both
Cationic acid cycle: H+ for K+
Anionic basic cycle: OH- for tartrate ion
Mixed treatment: two resins
Cation exchange reduces pH below 2  only treat portion of wine (10-20%); goal: final pH reduction ~0.2
Can affect color in red wines due to pH change
Works for all wines, low time and energy consumption

## Slide 8
Electrodialysis
Permeable membranes and electric field  ions move from wine to electrolyte in recirculation process
Electrodes enforce ion migration based on charge (endpoint determined by conductivity change
No effect on acidity and pH; reduction of Ca2+ and SO42- possible
Source:

## Slide 9
Mannoproteins
Only examples; more products available
Glycoproteins as natural part of S. cerevisiae cell wall
Work by inhibiting crystal expansion
Stability achieved around 25 g/hL, no degradation over time
Positive side effect: may stabilize proteins and other macromolecules as well (color?), provides mouthfeel

## Slide 10
Use in the industry (E 466):
Thickener in toothpaste and syrups, water binder in ice-cream and baked goods
Suspending aid in sauces, cosmetics, and beverages
And many many more
 Also widely used to stabilize tartrate in white wines and sparkling wines (legal limit: 100 mg/L)
Potassium bitartrate crystal
 CMC attaches to bitartrate crystals in solution and inhibits crystal growth  no precipitation
Carboxymethyl cellulose (CMC)

## Slide 11
Limited efficiency of CMC in red wine due to interaction with wine components (Moutounet et al. 2010, Sommer et al. 2016)
Crystals and turbidity in about 20 % of the red wines (Lasanta and Gómez 2012)
Protein instable wines tend to have more problems with haze
No prediction of haze formation possible
CMC producers do not recommend use in red wine
Very stable in white wines, no degradation
Long term protection
Limitations: check export regulations
 Development of new adapted products or application strategies for red wines

## Slide 12
Potassium polyaspartate (KPA)
Synthetic polyamide of L-aspartate
Inhibits crystal growth, no effect on color, no thermal degradation <40°C
Addition close to filtration possible (no effect on filterability)
Negative charge at wine pH  binds K+
Good long-term stability (1 year of storage)
Most studies do not find sensory impact

## Slide 13
Potassium polyaspartate (KPA)
Source: https://winesvinesanalytics.com/
Advantage over CMC  no effect on color

## Slide 14
Metatartaric acid
Source: https://www.eaton.com/
Internal ester of two tartrate molecules
Prevents crystal growth; more effective with higher esterification rate
Common addition at 10 g/hL to achieve stability
Problem: only temporary effect (ester hydrolyzes over time)  protection for max. 2 years
With ester hydrolysis increase in tartrate concentration  increased instability
Treatment only for wines in cold storage and with fast consumption

## Slide 15
Treatment option | Pros | Cons
Cold stabilization | Simple procedure, “non-invasive” method | Very time and energy consuming, filtration required
Ion exchange | Selective, easy to adjust | Limited by pH change (color), use of chemicals
Electrodialysis | Great process control, removal of Ca2+ and SO42- possible | Expensive equipment
Gum arabic | Simple addition, no filtration | Non-specific, unpredictable efficiency
Mannoproteins | Simple addition, no filtration | Possible color reduction
Carboxymethyl cellulose | Simple addition, no filtration | Only in protein-stable wines, not recommended in red wines
Potassium polyaspartate (KPA) | Simple addition, no known side effects | Limited long-term data

## Slide 16
This chart from Enartis compares the costs of using the new potassium polyaspartate products (KPA), compared to other cold-stabilization methods: GA = Gum Arabic; MP = Mannoprotein; CMC = Carboxymethyl cellulose; MTA = metatartaric acid; CE = Cation Exchange Resins -- Electrodialysis; Cold = Traditional cold method. Read more at: https://winesvinesanalytics.com/newsbriefs/article/194235/Two-New-Products-Stabilize-Tartrates-in-Wine Copyright © Wines & Vines
Enartis study placed crystal inhibitors as most cost effective
Cation exchange and electrodialysis most cost effective treatments

## Slide 17
Source: Lasanta and Gomez, 2012

## Slide 18
Protein removal strategies

## Slide 19
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Bentonite
Protein
Polyphenol
Principle of protein removal
Bentonite still the standard
Polysaccharides (Carrageenan; Irish moss) work with same limitations  better at low pH
Charge-based interactions much more specific and efficient
Stabilization of proteins also possible  mannoproteins

## Slide 20
Bentonite alternatives
Model wine trial
Wine trial (wide variety of wines)
n.s.
n.s.
n.s.
n.s.
*

## Slide 21
Conclusions
Most cost effective might not always be the best choice (example: CMC)
Non-additive treatment options: ion exchange and electrodialysis
Promising additive option: KPA (labelling requirements?)
Choice should be based on wine pH, color, expected shelf-life, cost analysis and export restrictions
Economy of scale important to balance equipment purchase costs and operational costs
Protein stabilization most effective with bentonite but options available to reduce usage and improve sustainability

## Slide 22
Thank you very much for your attention
Any questions?